## Slide 1: MassFUSIOn 2.0
Features & Requirements

## Slide 2: AGENDA
Introduction​
Primary goals
Product Perspective/Features
Design Approach
​Use Cases​

## Slide 3: introduction
The purpose of this document is to detail the requirements for a “MassFusion version 2.0” software. This formal document will be used to define the problem scope, proposed solution to the problem and intended use of the solution.

## Slide 4: PRIMARY GOALS
.
A web- based MassFusion 2.0
.
Application to manage the flow of load cell manufacturing ensuring quality and control
.
digital connectivity and integration with enterprise ERP and CRM applications to enhance productivity
.
digital tagging of each load cell in the production flow through serial number and bar code marking together with bar code scanning
.
quality tracking and reporting capabilities

## Slide 5: Product Perspective
Registration MANAGER
User Administration
MODeL MANAGER
Model design and engineering doc versions
PRODUCT MANAGER​
Production Workflow
Collection of Services

## Slide 6: Product perspective
Features
Platform : Web Based
  Creating and Editing of Models,
  Creating and Revision of Documents,
  Addition and Editing of Capacities
  Batch Tracking***
  Product History***
  Automatic Analysis***
  Engineering interfaces to Production Drawing and Procedures*
  Reports
    Event Reports
    Overview Reports
    VCap Reports
  Creating and deletion of users
  assignment of roles and functions.
* Model Management
* Production Management
  Loadcell Serial Number Generation
  Heat Treating
  Perform Chrome inspection,
  BarCode Label Printing***
  Gauging
  Gauging Inspection
  Wiring
  Cabling
  Trimming (Zero balance)***
  Exercise
  Add Resistor
  Sealing
  Auto Verification(Initial and Final
  Packaging
  Shipping
  Finished Product Electronic List
  Generation of edocuments for QuickBooks/Integration***
* User management

## Slide 7: USE CASES
Possible Interactions

## Slide 8: MODeL MANAGER use cases
MODeL MANAGER
Model design and engineering doc versions
Got the Specs ?

## Slide 9: MODEL MANAGEMENT

## Slide 10: CASE 1
Use Case | Model Management- New Model Type
Actors | Design Engineer
Tasks | Add a new model type to the system (eg Axle Pad, Ultra Slim etc) .
Add New Model Type ***

## Slide 11: CASE 2
New Model and Capabilities
Use Case | Model Management- New Model and Capabilities
Actors | Design Engineer
Tasks | Add a new model to the system Define model capacities Define test parameters (number of points, testing/measuring range, etc) Define nominal output

## Slide 12: CASE 3
Use Case | Model Management- Add Document
Actors | Design Engineer
Tasks | Select an existing model Add first version of a document
Add Document

## Slide 13: CASE 4
Model Revision
Use Case | Model Management- Model Revision
Actors | Design Engineer
Tasks | Select an existing model Select an existing document Add a new revision of selected document Associate a change order with the new revision Specify which capacities of the model the revision pertains to

## Slide 14: CASE 5
Batch Tracking***
Use Case | Model Management– Batch Tracking
Actors | Design Engineer
Tasks | Select an existing model Select an existing Batch Number Perform Tracking and searching for purposes of reporting and analysis

## Slide 15: CASE 6
Use Case | Model Management– Perform Analysis
Actors | Design Engineer
Tasks | Select an existing model Select other related parameters Perform Automatic Analysis – statistical analysis for data generated during AV
Perform Analysis***

## Slide 16: CASE 7
Access Engineering Drawing
Use Case | Model Management– Access Engineering Drawing
Actors | Design Engineer
Tasks | Viewing of design documents for production (implemented in Massfusion 1.0 upgrades)

## Slide 17: CASE 8
Assign Serial No
Use Case | Model Management– Assigning Serial No
Actors | Receiver
Tasks | Select an existing model Select an item quantity Enter the certification number of the steel , assign a BatchNo *, and other summary text Accept and confirm parameters Note: Batch of load cells is a grouping/set of shells received into Massload from which serial numbers will be generated

## Slide 18: PRODUCTION MANAGEMENT use case
PRODUCT MANAGER​
Production Workflow
Let’s build it

## Slide 19: PRODUCTION MANAGENT
Selection of loadcell at any stage shall be done by with Barcode scanner with keyboard backup alternative
Login shall be done with Barcode scanner

## Slide 20: CASE 1
Print BarCode Label***
Use Case | Production – Printing of Barcode Label
Actors | Assemblers
Tasks | Select a product or a batch Print Label
PreCondition | BarCode Printer Must be connected

## Slide 21: CASE 2
Production – Production – Chrome, Gauging, Gauge inspection, Wiring, Cabling, Zero Balancing*, Exercise, Add Resistor and Sealing
Use Case | Production – Production – Chrome, Gauging, Gauge inspection, Wiring, Cabling, Zero Balancing*, Exercise, Add Resistor and Sealing
Actors | Assemblers
Tasks | Select a product in the user’s current production stage View latest versions of design documents relevant to the user’s current production stage Pass the product onto the next production stage (or fail if applicable: Perform Non Conformance Notification )

## Slide 22: CASE3
Initial Verification
Use Case | Production – Initial Verification
Actors | Assemblers
Tasks | Select an existing product in the “Initial Verification” stage of production. Install the indicated test jig onto the tester. Install the chosen product onto the test jig. Commence automated testing. Pass the product onto the next production stage, or fail if the results do not fall within the tolerance values specified by the model design, perform Non Conformance Notification
PreCondition | Agilient Multimeter, MoreHouse and RMC Tools must be connected

## Slide 23: CASE 4
Final verification
Use Case | Production – Final Verification
Actors | Assemblers
Tasks | Select an existing product in the “Final Verification” stage of production. Install the indicated test jig onto the tester. Install the chosen product onto the test jig. Commence automated testing. Pass the product onto the next production stage, or fail if the results do not fall within the tolerance values specified by the model design.
PreCondition | Agilient Multimeter, MoreHouse and RMC Tools must be connected

## Slide 24: CASE 5
Non Conformance Notification
Use Case | Production – Non-Conformance Notification
Actors | Assembler, Production Manager
Tasks | Assembler performs inspection or verification on the product. The product fails. A notification record is inserted into the database. Notification is presented to the Production Manager via the software.*

## Slide 25: CASE 6
Packaging
Use Case | Production – Packaging
Actors | Assembler, Production Manager
Tasks | User Select Product Print Certificate Print Warranty

## Slide 26: CASE 7
Generate QuickBooks Electronic Document***
Use Case | Production – Generate QuickBooks Electronic Document
Actors | Assembler
Tasks | Select a product or Products Generated electronic document

## Slide 27: CASE 8
Scrapping/Team Leader Decision
Use Case | Production – Non-Conformance Notification
Actors | Production Manager
Tasks | Assembler performs inspection or verification on the product. Select a product of interest Move product to desire stage OR Add a comment Scrap product A notification record is inserted into the database.

## Slide 28: CASE 9
Tracking
Use Case | Production – Tracking
Actors | Assembler, Production Manager, Designer,
Tasks | Select a product Type search criteria Search System should display product details ,current stage and events journey

## Slide 29: CASE 10
Shipping
Use Case | Production – Shipping
Actors | Shipper
Tasks | Connect with QuickBooks Select product Select customers Ship

## Slide 30: Production FLOW

## Slide 31: REGISTRATION MANAGEMENT use case
Registration MANAGER
User Administration
Identify Yourself Please
You can only access these rooms

## Slide 32: REGISTRATION MANAGEMENT

## Slide 33: CASE 1
Registration User Creation
Use Case | Registration: Create Account
Actors | Administrator
Tasks | Create user name Select a role for user System generates default password for user Assign permissions to user

## Slide 34: CASE 2
Reset User Details
Use Case | Registration- Reset User Details
Actors | Administrator
Tasks | Select a user Update user record

## Slide 35: CASE3
Deactivate Account
Use Case | Registration Deactivate Account
Actors | Administrator
Tasks | Select a user Deactivate account Update user record

## Slide 36: CASE 4
Assign Permissions
Use Case | Registration : Assign Permissions
Actors | Administrator
Tasks | login Assign /remove permission Update user credential

## Slide 37: CASE 5
User Password Management
Use Case | Registration: Password Management
Actors | User
Tasks | login Modify password Update user credential Note – This can only be done by the account owner

## Slide 38: summary
……

## Slide 39: QUESTIONS/ CONTRIBUTIONS